## Slide 1: Towards a True Energetically Sustainable WSN: A Case Study with Prediction-Based Data Collection and a Wake-up Receiver
Alessandro Bogliolo, Valerio Freschi, Emanuele Lattanzi, Amy L. Murphy and Usman Raza
Notes: Energetic Sustainable
Power consumption Model….
Title… and
Simulator evaluation details are missing altogether
Gp’s
- wakeup radio prototypes
- motivate case study with that
No details of 380 and wakeup receiver !!!!!
JUSTIFY!
Define baseline

## Slide 2: A Motivating Case Study: Adaptive Lighting with WSNs
Lamp levels typically statically determined, ignoring environmental
  Overprovisioned to meet the regulations
Problems: waste energy and potential security hazard
Idea: place wireless sensors along tunnel, adjust lamps to actual conditions
  Eliminate overprovisioning, account for environmental variations
stop distance
Notes: Put it
How it is typically done
Objective: day time, It is not to dark ..
Night not too bright
driver
Statically over provisions the light
Over provisions
Ponte alto and its statistics

## Slide 3
2-lane carriageway
Tunnel length of 260 m, 40 battery powered WSN nodes
Full, operational system described in IPSN’11

## Slide 4: Goal: Using Renewable Energy for Achieving a Long Term Operation
Currently, nodes are powered with disposable batteries
Problem:
  Short lifetime
  Replacement is expensive, labour intensive and a safety hazard
Goal: long term operation with rechargeable batteries and energy harvesters
Lifetime
Notes: shortnen
Wanna get rid of batteries
Batteries are expensive

## Slide 5: Goal: Using Renewable Energy for Achieving a Long Term Operation
Currently, nodes are powered with disposable batteries
Problem:
  Short lifetime
  Replacement is expensive, labour intensive and a safety hazard
Goal: long term operation with rechargeable batteries and energy harvesters
Lifetime
Harvestable energy is two orders of magnitude less than the power consumption
Notes: Put text

## Slide 6: Approach: A Software Hardware Co-design for Minimizing Energy Consumption
Harvester
VirtualSense
Prediction Based Data Collection
Dynamic Power Management
Wakeup
Receiver
Photovoltaic
1
2
3
Software
Hardware
Notes: It also defines the layout
Add Sotware hardware labels
Add the numbers

## Slide 7: Evaluation Methodology
Power consumption model
  Functional state diagram
  Empirical hardware measurements
Model described in ENSSys’13
Network traffic
  Actual data from the tunnel
  47 days, 1 sample every 30s, 5.4 million measurements
Multiple data collection trees
Notes: Data collection trees bias unfairly
Forwarding
+
Particular wakeup re
Tree

## Slide 8: 1: Prediction Based Data Collection
time
Typical WSN System
Sink gathers all sensor readings of the WSN.
Advantage: precise
Prediction Based Data Collection/ WSNs
Sink predicts sensor readings of the WSN.
Advantage: less traffic
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
1
Notes: Exactly same data ------------------ A lot of DATAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAAA
actual
less
Sink GATHERS
Sink PREDICTS

## Slide 9: 1: Prediction Based Data Collection
Derivative Based Prediction (DBP)
  A linear model: Easy to compute
  Excellent data approximation
99% reduction in data traffic
  saves radio communication cost
Sensor value
δ
Time
DBP is described in PerCom’12
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
1
DBP Model
Notes: Congestion
Overhearing
Communication cost
PBDC
DPM – Energy saving
Wakeup receiver: periodic receive checks, transmission times & receptions times

## Slide 10: Lifetime Improvement
No. | Dynamic Power Management |  | Wakeup Receiver | Lifetime Improvement | 
 | MCU | Radio |  | Periodic | DBP
1 | Standby | LPM1 | No | 1x | 1.7x
Standard hardware + NO software Optimization = Baseline
DBP almost doubles the lifetime
Standard Hardware
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
1
Notes: What this table is????
Software hw

## Slide 11: 2: VirtualSense
Ultra low power platform
  Ideal for energy harvesting WSNs
Features
  Dynamic power management
  Novel wakeup receiver
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2
VirtualSense Node
Notes: Focus on next
Treat it as outline

## Slide 12: 2.1: Dynamic Power Management (DPM)
Microcontroller: TI MSP430f54xx
  Turn off components between idle periods (infrequent transmissions of DBP models)
  Power consumption varies from 0.66nW and 10mW
Radio: CC2520 RF Transceiver
  Deep sleep mode (LPM2)
    Infrequent transmissions of DBP models
    Current draw (~0.1 uA) in receive mode
  Frame Filtering
    Allows discarding unintended packets
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2
Notes: Hints to case study ??
FF: “unicast” unintendedpackets

## Slide 13: Lifetime Improvement
No. | Dynamic Power Management |  | Wakeup Receiver | Lifetime Improvement | 
 | MCU | Radio |  | Periodic | DBP
1 | Standby | LPM1 | No | 1x | 1.7x
Standard Hardware
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
1

## Slide 14: Lifetime Improvement
No. | Dynamic Power Management |  | Wakeup Receiver | Lifetime Improvement | 
 | MCU | Radio |  | Periodic | DBP
1 | Standby | LPM1 | No | 1x | 1.7x
2 | Standby | LPM2 | No | 1.7x | 7.8x
3 | Standby | LPM2+FF | No | 2x | 7.8x
4 | Sleep | LPM2 | No | 1.7x | 7.9x
5 | Sleep | LPM2+FF | No | 2.0x | 7.9x
Improvement not two orders of magnitude: Not energetically sustainable !!!
Multiple DPM configurations
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2
Notes: Not energetically
Did a lot got little
Radical

## Slide 15: 2.2: Wakeup Receiver
Uses ultra sound technology
Out of band triggering
  turns ON expensive data transceiver only for data receptions.
Ultra-low energy consumption
  Rx: 820nA vs. 18.5mA for primary data radio
Range 14m
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2
Ultrasound Wakeup Receiver
Notes:     Could not find comparable numbers

## Slide 16: 2.2: Wakeup Receiver
Tx
Rx
Sender
Receiver
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2
Without
Energy Efficiency: No receive checks and shorter Tx
Dominant receive checks
Shorter
Rx
Sender
Receiver
Trigger
Tx
With
Wakeup receiver ON
Notes: Add Animation
Border
Too much blue
Fix it visually
awefull

## Slide 17: Lifetime Improvement
No. | Dynamic Power Management |  | Wakeup Receiver | Lifetime Improvement | 
 | MCU | Radio |  | Periodic | DBP
1 | Standby | LPM1 | No | 1x | 1.7x
2 | Standby | LPM2 | No | 1.7x | 7.8x
3 | Standby | LPM2+FF | No | 2x | 7.8x
4 | Sleep | LPM2 | No | 1.7x | 7.9x
5 | Sleep | LPM2+FF | No | 2.0x | 7.9x
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2

## Slide 18: Lifetime Improvement
No. | Dynamic Power Management |  | Wakeup Receiver | Lifetime Improvement | 
 | MCU | Radio |  | Periodic | DBP
1 | Standby | LPM1 | No | 1x | 1.7x
2 | Standby | LPM2 | No | 1.7x | 7.8x
3 | Standby | LPM2+FF | No | 2x | 7.8x
4 | Sleep | LPM2 | No | 1.7x | 7.9x
5 | Sleep | LPM2+FF | No | 2.0x | 7.9x
6 | Sleep | LPM2 | Yes | 2.6x | 
+ Wakeup Receiver
Modest improvement- huge traffic
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2
Notes: A lot of traffic tx + fws 2.6 eliminating benefit

## Slide 19: Lifetime Improvement
No. | Dynamic Power Management |  | Wakeup Receiver | Lifetime Improvement | 
 | MCU | Radio |  | Periodic | DBP
1 | Standby | LPM1 | No | 1x | 1.7x
2 | Standby | LPM2 | No | 1.7x | 7.8x
3 | Standby | LPM2+FF | No | 2x | 7.8x
4 | Sleep | LPM2 | No | 1.7x | 7.9x
5 | Sleep | LPM2+FF | No | 2.0x | 7.9x
6 | Sleep | LPM2 | Yes | 2.6x | 380x
+ Wakeup Receiver
Two order of magnitude improvement with DBP + wakeup reeciver
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
2

## Slide 20: 3: Harvester – Energetic Sustainability?
Chart: Node
Harvested | 2474.9222 | 1522.6502 | 842.6761 | 545.7805 | 615.69 | 486.5461 | 691.2264 | 409.5964 | 689.3815 | 530.7269 | 540.9752 | 176.0711 | 116.4838 | 305.8979 | 193.3605 | 147.7566 | 147.7566 | 25.2388 | 16.8909 | 15.8902
Harvested
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
3

## Slide 21: 3: Harvester – Energetic Sustainability?
Chart: Node
Harvested | 2474.9222 | 1522.6502 | 842.6761 | 545.7805 | 615.69 | 486.5461 | 691.2264 | 409.5964 | 689.3815 | 530.7269 | 540.9752 | 176.0711 | 116.4838 | 305.8979 | 193.3605 | 147.7566 | 147.7566 | 25.2388 | 16.8909 | 15.8902
Harvested
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
3

## Slide 22: 3: Harvester – Energetic Sustainability?
Harvested
Hardware
Chart: Node
Harvested | 2474.9222 | 1522.6502 | 842.6761 | 545.7805 | 615.69 | 486.5461 | 691.2264 | 409.5964 | 689.3815 | 530.7269 | 540.9752 | 176.0711 | 116.4838 | 305.8979 | 193.3605 | 147.7566 | 147.7566 | 25.2388 | 16.8909 | 15.8902
Consumed (No-DBP) | 1368.528 | 3690.3082 | 3095.4709 | 3357.4942 | 4914.217 | 3559.9756 | 3050.8324 | 4472.1301 | 2152.783 | 3184.6509 | 2476.0785 | 2565.7881 | 2383.4736 | 2066.9216 | 1802.3632 | 1332.1202 | 1118.983 | 824.0791 | 562.1018 | 250.7573
Not energetically sustainable
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
3

## Slide 23: 3: Harvester – Energetic Sustainability?
Chart: Node
Harvested | 2474.9222 | 1522.6502 | 842.6761 | 545.7805 | 615.69 | 486.5461 | 691.2264 | 409.5964 | 689.3815 | 530.7269 | 540.9752 | 176.0711 | 116.4838 | 305.8979 | 193.3605 | 147.7566 | 147.7566 | 25.2388 | 16.8909 | 15.8902
Consumed (No-DBP) | 1368.528 | 3690.3082 | 3095.4709 | 3357.4942 | 4914.217 | 3559.9756 | 3050.8324 | 4472.1301 | 2152.783 | 3184.6509 | 2476.0785 | 2565.7881 | 2383.4736 | 2066.9216 | 1802.3632 | 1332.1202 | 1118.983 | 824.0791 | 562.1018 | 250.7573
Consumed (DBP) | 19.5687 | 20.3445 | 18.6975 | 18.128 | 16.7692 | 15.5463 | 14.8993 | 14.7353 | 14.427 | 14.358 | 14.2668 | 14.2155 | 14.1768 | 14.1568 | 14.1242 | 14.1082 | 14.105 | 14.1022 | 14.101 | 14.0995
Harvested
Hardware
Hardware+Software
Energetically sustainable even for nodes with least harvestable energy
Harvester
VirtualSense
Software
DPM
WURx
Photovoltaic
3

## Slide 24: Conclusion
Harvester
VirtualSense
Prediction Based Data Collection
Dynamic Power Management
Wakeup
Receiver
Photovoltaic
Lifetime
Notes: It also defines the layout
Add Sotware hardware labels
Add the numbers

## Slide 25: Conclusion
This is only the beginning…
  Short range of wakeup receiver: dense deployment
  Directional wakeup receiver: fixed tree/ robustness?
  Analytical model is promising, real node evaluation is needed
Even though it is a case study, results are potentially wide
  DBP is generally applicable to WSNs
  Tunnel = data collection, common in most WSNs
  VirtualSense hardware is modular: expandable
Not to forget, we got excellent results!
  380 x improvement  ∞ lifetime

## Slide 26: Thank you raza@fbk.eu

## Slide 27: Data reduction with DBP